## Slide 1: Recovery after a HAZMAT incident
Module 5
Hospital HAZMAT Curriculum
Operations Training

## Slide 2: Objectives - Recovery
Staff rehabilitation
Securing the room and equipment
Valuables and clothing
Cleaning and washwater
Notifying the proper authorities
Debriefing and CISM

## Slide 3: Recovery Phase
Focus shifts from acute injury and illness to recovery
Need to begin to plan for recovery even during response phase
Hospital staff physical and emotional needs are priority
Notes: <number>
The recovery phase is often the least attended to of the phases of disaster, but can be the most important in many ways!

## Slide 4
Notes: <number>
Plain water is the best for hydration. Avoid soda and other high-sugar or caffeinated liquids.
Hydration for all team members

## Slide 5
Notes: <number>
A medical evaluation including full vital signs and screening medical exam is important for each team member after leaving the warm zone.

## Slide 6
Secure the room
and other areas
that are in the
warm zone
Notes: <number>
Control of the areas that are ‘warm’ and consultation with HAZMAT Group Supervisor / Safety manager is important to determine what needs to be done.

## Slide 7: Valuables and Clothing
When possible, try to secure in room
If not, secure in other ‘warm’ area
Assure that patients and bags are appropriately numbered
Depending on incident may be able to return:
  Everything
  Nothing
  Valuables that can be washed, but not leather or other absorbent items
Notes: <number>
Do NOT guarantee patients ANYTHING regarding their belongings. In most cases, they will be able to get them back, but in some, everything may need to be destroyed.

## Slide 8: Cleaning the ‘Warm’ Area
Discuss with poison control and hazardous materials branch director (safety director) whether requires outside assistance
Hospital safety director can obtain contractor assistance for cases where disposal/clean up is beyond facility capabilities

## Slide 9: Equipment and Facility Decontamination
External resources capable of testing contaminated run off and cleaning equipment and facility
  Sample gathering and testing
  Recommendations for cleaning equipment and facilities
  Resources for cleaning equipment and facilities
  Time consuming and costly

## Slide 10: Clean-up
When internal clean up is possible:
  Follow instructions from HAZMAT group leader and poison control
  In general, mop and wipe surfaces with 1:10 household bleach : water
  Ventilate areas to outside – may need fans in shipping container outside Special Care
  Respirators may be wiped down with bleach solution diluted 1:10, discard canisters unless otherwise instructed.

## Slide 11: Clean-up
When internal clean-up is not possible:
  Consult with HAZMAT supervisor to determine appropriate actions
  Seal off areas that are contaminated as possible
  If not possible to seal certain areas (eg: carpeting that needs cleaning) may consider covering with heavy plastic sheeting and taping edges

## Slide 12: Washwater
If contaminated washwater went down drain notify:
  State Duty Officer (SDO) 651-649-5451
  Duty Officer will notify appropriate regulatory agencies (eg: Metropolitan Environmental Services Council, EPA)
Contained washwater barrels should be capped awaiting disposition
Notes: <number>
It is much better to divert washwater down sanitary sewer rather than storm sewer due to the processing that the treatment plants perform. Storm sewers usually enter directly into the watershed.

## Slide 13: Draining the tubs
Notes: <number>
A pool pump (battery operated) may be used to drain the tubs, or they may be poured using a large funnel (and large personnel to lift). Washwater ideally should be contained in sealed barrels following an event and held for testing to see if the chemicals present really do present a hazard (rare).

## Slide 14: Notifications
Hospital safety manager
Wastewater notifications
Hospital administration

## Slide 15: Documentation
Assure each patient decontaminated has the process documented in their nursing charting for billing and clinical purposes
Document staff involved for Safety Dept. / Employee Health and complete paperwork as needed for any adverse events or incidents that occurred
Notes: Picture?
<number>

## Slide 16: Restocking
Assure that suits / gloves / boots are re-stocked with respirators
Assure battery use is documented on single-use batteries and NiCad batteries are recharged

## Slide 17
Notes: <number>
Managing stress for the provider is a critical part of the recovery process.
PFA

## Slide 18: CISM Components
Comprehensive, systematic, and multi-tactic approach to managing traumatic stress within an organization or community
Pre-event: Education, planning, protocol development, policy development
NOT the same as response critique
Notes: <number>
Critical incident stress management is a tool that can be used to defuse stress after an incident.

## Slide 19: CISM Components
During event: On-scene support services, one-on-ones, advice to command, support to staff
Post-event: One-on-ones, defusing, group sessions, spouse support, follow up services
Metro CISM team contact:
  West Metro MRCC 612 347 2123

## Slide 20: Critique and Evaluation
Diffuse staff as needed
Debrief staff following rest, hydration, and nutrition
Formal critique of event with all staff who were involved as needed
Review current plans, revise as needed
Share lessons learned
Notes: <number>
The evaluation of the event should lead to changes in practice/planning for the next event.
Initial debrief or ‘hotwash’ should capture initial reactions as to what went well/poorly – a review sheet should be completed EVERY TIME the decon room is used for a hazmat incident
Formal critique may involve additional interviews, examination of equipment, etc. and a written after-action plan may be developed depending on the size of the incident

## Slide 21: Recovery Pearls
Attend to the physical and psychological needs of staff
Notify the proper authorities if washwater sent down the drain
Secure the warm areas
Figure out what to do with the ‘warm’ stuff
Restock
Debrief, learn, adjust response plans