## Slide 1: Introduction to Hazardous Materials
Module 1
HCMC Hospital HAZMAT Curriculum
Operations Training
Notes: <number>
Module 1 provides an overview of hazardous materials and meets many of the OSHA requirements for awareness level training.

## Slide 2: Introduction
Overview of HAZMAT training
Hazards of HAZMAT
Recognition
Physical Properties
Information Sources
Risk Assessment
Containment

## Slide 3: HAZWOPER
OSHA’s Hazardous Waste Operations and Emergency Response regulations
29 CFR 1910.120
Specify training, response, etc. for hazmat releases
Hospital personnel are NOT HAZMAT teams if only performing decon or defensive management of spills
Notes: <number>
OSHA’s interpretation is that hospital personnel do not require as extensive training in site/scene control if we are providing only decontamination services.

## Slide 4: HAZWOPER - Training
Incident Management System (eg: HICS, NIMS IS100-HC, IS200-HC)
On-site Incident Commander (Victim Decon Unit Leader or HAZMAT Branch Director) (24h cumulative)
Operations – decon team members
Awareness – likely to discover / report an incident
Hazard Communication – all employees
Skilled Support Personnel
Notes: <number>
On-site incident commander does not have to be on site for hospital decontamination operations to begin. Most ED employees need to be trained to awareness level, decontamination team members to operations level. Skilled support personnel are those whose specific skills in the ‘warm zone’ could not be anticipated, but is needed during an incident – in that case a briefing may be given, the person assisted with PPE and closely monitored in the ‘warm zone’ without prior training (eg: cardiothoracic surgeon?). Hazard communication is information given to all employees about hazards in their workplace.

## Slide 5: Operations Training
8 hours or ‘to competency’
Annual refresher training required
Integrated into hospital/safety education program
Must have as part of PPE program:
  Respiratory protection program
  Medical surveillance program
Notes: <number>
If the institution carefully defines its competencies, training could be accomplished in less than 8 hours, but this is an accepted minimum for most training programs. The employee must demonstrate competence with both didactic and practical measures and agree with his employer that he/she is comfortable with all the materials and practical skills and has no further questions regarding their role in a response. There is no guidance on the necessary scope of the medical surveillance program, as that for HAZMAT teams would not seem to apply, but team members health must be surveyed at regular intervals so they do not pose a risk to themselves and others.

## Slide 6: Operations Objectives
Basic hazard recognition and mitigation
Risk assessment
Personal protective equipment (PPE)
Hazardous Materials terminology
Basic decontamination procedures
Institutional procedures
Recovery procedures
Notes: <number>
These objectives are defined in the HAZWOPER standard 29CFR1910.120 (see www.osha.gov)

## Slide 7: Modules
Intro to HAZMAT
Institutional Protocol
PPE
Patient presentation and decontamination
Recovery
Review
Hqmeded.com/hazmat

## Slide 8: Who are the key personnel?
Safety manager – oversight / program
Facilities – ventilation, decon area
ED staff - decon
  Health care assistants
  Resident physicians
  Nurses
Employee Health – medical surveillance, respiratory protection program
Notes: <number>
Safety manager is the keystone, makes sure that the education and competency program is functioning well and integrates with response plan at facility. Facilities makes sure decon area is functional. ED staff are responsible for decon at our facility. EHS is responsible for respirator and hazmat medical surveillance programs in conjunction with the safety manager.

## Slide 9
CLOSED
Notes: <number>
Mismanagement of HAZMAT incidents may result in closure of part of or even all of a facility.

## Slide 10: Means of Hospital Arrival - Tokyo
Notes: <number>
The vast majority of victims from the sarin attack in Tokyo in 1995 self-referred to the hospital. 361 came on foot or by private vehicle, only a few arrived by fire vehicles or ambulance. Hospitals must be prepared for large numbers of self-referred contaminated patients from incident scenes.

## Slide 11: Are HAZMAT events common?
13 states participating in ATSDR registry
2005 - 8,603 events
Location
  Fixed facility 74%
  Transportation 26%
Most common release – inorganic and volatile organic compounds
89.9% single agent
Notes: <number>
ATSDR – Agency for Toxic Substance and Disease Registry
Fixed facility could include home, other locations
Photos – fixed and transportation? Large slide 90%?

## Slide 13: Fixed facility

## Slide 15
Notes: 2.1 on richter scale, windows blown out up to 7 miles away
<number>

## Slide 16
Notes: 15 dead, 160 injured, 150 buildings damaged
Plant last inspected by OSHA in 1985 and fined $30 for improper storage of anhydrous ammonia
<number>

## Slide 17
Notes: Festus, MO – injured 3 and sent 63 to hospital for evaluation
<number>

## Slide 18: Injuries from HAZMAT
2,034 victims in 778 events (9% of all events)
3.4% victims died
85% injured at fixed facility
29.4% of injuries from Chlorine
184 responder injuries
  hospital personnel injuries <2% of responders – respiratory irritation from irritant gases predominated
Notes: <number>
Injuries are not common in hazmat incidents. Most injuries occurred at known facility, chlorine is a very common agent and commonly causes respiratory irritation. Very few injuries are to hospital personnel and most of these involved transient irritation of the airways.
Chlorine picture slide?

## Slide 19: Injuries from HAZMAT
Respiratory irritation 30%
Headache 15%
Dizzy / neurologic 13%
Eye irritation 9%
GI symptoms 10%
HSEES / ATSDR 2005
Notes: <number>
Most injuries are due to respiratory irritation, of these, almost all are transient effects. The majority of victims who seek medical care do so because of inhaled agents. Inhaled agents tend to often induce psychosomatic symptoms in large numbers of people, regardless of the scope of the initial release. Burns are uncommon, but often result in more lasting injury than vapor/gas exposures.

## Slide 20: Patient Disposition
15% patients released at scene
52% patients transported and released
< 10% admitted
3% fatalities (2 of 69 deaths after hospital arrival)
Key principle
  Most hazmat victims are not seriously ill
Notes: <number>
Nearly all victims that were brought to the hospital were discharged. For inhalant exposures, those who arrive to the hospital with vital signs almost universally have good outcomes.

## Slide 21: Definition
OSHA definition: Hazardous Chemical: Any substance to which exposure “results or may result in adverse affects on the health or safety of employees:” or “any chemical which is a physical hazard or a health hazard.” 29 CFR 1910.1200 (c)
Notes: <number>
There are many different definitions of a Hazardous Material.
OSHA’s is as listed above. Basically, it’s a hazard if it has the potential to harm you if it gets in contact with you in too high a dose (remember, most things are poisons, it just depends on the amount! – consider ethanol, for instance!)

## Slide 22: Hazards…
Chemical
Nuclear/Radiological
Biological
Explosives & Incendiary Devices
Notes: <number>
There are many acronyms for classifying a Mass Casualty Incident (MCI) such as:
WMD = Weapons of Mass Destruction
NBCE = Nuclear Biological Chemical Explosives
BNICE = Biological Nuclear Incendiary Chemical Explosives

## Slide 23: Recognition of hazard
Known exposure or spill
Clinical presentation
  Respiratory distress, altered consciousness, or cholinergic syndrome (miosis and respiratory/secretory symptoms)
  Skin burns / irritation
  Odor or physical contaminant observed
Notes: <number>
Many, if not most, exposures presenting to the hospital are to unknown agents. Treatment of the clinical syndrome is a higher priority than trying to figure out exactly what caused the symptoms. Above all, do NOT miss a cholinergic syndrome – small pupils, secretions, and difficult respirations (plus fasciculations / seizures if you’re a stickler for more clues). These patients need antidotes AND are a very high risk to you until decontaminated!

## Slide 24
Notes: Festus, MO – injured 3 and sent 63 to hospital for evaluation
<number>

## Slide 25: Scene Clues
Not always reported as hazmat incidents!
  Multiple persons with similar symptoms or collapsed
  People running from area
  Evidence of a leak
  Fire
  Vapors visible
  Unusual colors/ odors
Notes: <number>
Multiple persons affected should ALWAYS prompt consideration of a toxic agent.
Better picture?

## Slide 26: Response Issues
Any one of these factors can affect the safety of response:
  Time - eg: off-gassing
  Volume of Spill - Surface area
  Concentration
  Ventilation - Type and location
  Spill Control Product - Some work better than others
  Personnel Location - closer= worse
Notes: <number>
If it has just occurred, maybe the liquid has not emitted many vapors (fumes) yet, you may be able to intervene before the vapors get bad. Or if it has been awhile, maybe the vapors have dissipated. How good is the ventilation and where is the ventilation going? Spill control products should NOT be used unless you are very familiar with them.
VI. Spill Control products (Neutralizers)- do you have any?
VII. Personnel location - or patient location. Is the spill in an
isolated area? Or is it next to a bunch of offices, or next to
patients.

## Slide 27: Routes of Exposure
  Inhalation
  Absorption
  Ingestion
  Injection
Notes: <number>
Health can be compromised by contact with numerous substances if a dose is delivered into the body. A piece of wood sitting on your hand causes no harm, but if that same piece of wood was ground up into 5-50 micron size particles and was inhaled into the respiratory system, infection/pneumonia could result. Ingestions of toxic agents in suicide attempts can result in off-gassing (especially from vomit and secretions). Injection is very rare.
Absorption can be through broken or intact skin or mucous membranes (benzene vapor)

## Slide 28: Health Risk
Reaction depends on Dose at target organ site.
Risks depend on:
  Amount of substance contacted
  Type of substance
  Length of time exposed
  Predisposition of person exposed (ie.asthma)
Categorized as:
  Acute - short exposure, short term effects
  Chronic - long term exposure (usually small doses, long term effects - could be latent (ie.cancer)
Notes: <number>
Most anything in a large enough amount will be toxic (oxygen, for instance, causes lung damage when given at high concentrations for a prolonged period). Age and underlying health are critical factors – healthy patients may easily tolerate toxic challenges that critically injure those with pulmonary or cardiac disease.

## Slide 29: Primary Contamination
Contamination of people or equipment due to direct contact with the initial release of a hazardous material
Notes: <number>
This gentleman, and others at the scene, experienced primary contamination. Exposure to the source of a release can be very dangerous.

## Slide 30: Secondary Contamination
Contamination of a healthcare provider or equipment by direct contact with a contaminated patient or equipment remote from the release site
  Contact with adherent solids or liquids
  Exposure to off-gassing
Notes: <number>
Secondary contamination is magnitudes less than that experienced at the site of release, as it is removed from the site and the patient has undergone some ‘air decontamination’ enroute to you. The clothing is the primary reservoir for contaminants. Goal is to prevent contamination of rescuer and minimize exposure.

## Slide 31: Health Hazards
External Hazards
  Skin Contact
    Corrosive = React with skin (battery acid, caustic soda)
    Cryogenic = freeze skin (liquid O2 & N2)
    Flammable
    Radiation
Notes: <number>
Corrosives degrade the proteins of the skin,
Cryogenics freeze the cells and can kill them,
Flammable compounds cause heat burns
Radiation in high enough levels also can cause heat burns.

## Slide 32: Health Hazards
Internal Hazards
  Irritants
  Asphyxiant – simple and chemical
  Cholinergic
  Hydrocarbon
  Carcinogen
  Radiation
Notes: <number>
Irritants can cause inflammation, pain, redness, etc especially within the respiratory system, or mucous membranes.
Asphyxiants displace oxygen but are not necessarily toxic by themselves. Carbon dioxide displaces oxygen so it is not available for respiration, but carbon monoxide is inhaled and it binds to the hemoglobin so competes with oxygen in the red blood cells (chemical asphyxiant).
Cholinergic agents can be everyday pesticides (parathion, organophosphates) or chemical warfare agents such as Sarin.
Carcinogens are which shown to cause cancer..eventually…but not immediate. Coal tar, benzene, PCBs, UV radiation, cigarette smoking, are just a few.
Radiation comes in many forms both natural (i.e..from the sun and strata of the earth which contains various amounts of radioactive substances such as uranium) and man-made (mostly medical devices and procedures but also nuclear power plants and bombs). Radiation exposure is only harmful to living tissues if the dose reaches certain levels. Some radiation from UV light is considered to be beneficial.

## Slide 33: Toxicity Relationships
25000
200
Safe
Unsafe
Dangerous
Methanol
Methanol
Safe
1200
35
Unsafe
Carbon
Monoxide
Dangerous
CO
25
300
Safe
Unsafe
Dangerous
Ammonia
Ammonia
Safe
100
10
Dangerous
H2S
HCL
Unsafe
H2S
10
0.5
Un.
Dangerous
Chlorine
Safe
Chlorine
5
0.1
Un.
Dangerous
Acrolein
S.
Acrolein
Dangerous
0.00001
0.0001
VX
VX
Notes: <number>
Toxicity is relative, almost anything is toxic if you get too much, but some compounds are extremely toxic at all exposure levels (eg: VX). Green = safe, yellow = unsafe, red = dangerous exposure levels. Note the contrast between methanol and VX.

## Slide 34: Important Properties of Hazardous Materials
Chemical Names and Numbers
State of Matter
Solubility
Vapor Pressure
Flammability
Warning Properties
Notes: <number>
We will discuss each of these in greater detail in subsequent slides.

## Slide 35: Chemical Names & Numbers
  Chemical
  Common
  Generic
  Brand (proprietary)
Multiple names lead to confusion
CAS registry number
  Unique # for each atom, molecule, and mixture
Identify a chemical by
  Name
  CAS number
Spell similar sounding names
Notes: <number>

## Slide 36: State of Matter
Solid
  Fixed volume and shape
  Typically stays in one area
  Secondary contamination risk
  Melting point
Gas
  Variable volume and shape
  If released, widely dispersed
  No significant secondary contamination risk
Liquid
  Fixed volume, variable shape
  Flows downhill
  Secondary contamination risk
  Boiling point
Notes: <number>
Note that nerve agents should be treated as a vapor, not a gas exposure. Those patients exhibiting a cholinergic toxidrome should receive decon. Other gas exposures generally require no decontamination except clothing control.

## Slide 37: Solubility
Like dissolves like
Water-soluble
  Miscible
  Polar
  Ammonia, methanol, acetone, etc.
Nonwater-soluble
  Immiscible
  Nonpolar
  Hydrocarbons, carbon disulfide, etc.
  What do we do about nonwater soluble agents?
Notes: <number>
Water soluble – water will decon alone. Non-water soluble – requires soap – effective for nearly all agents.

## Slide 38: Vapor
Gaseous dispersion of a liquid or solid
Produced by evaporation of a liquid or solid
Sublimation
  Solid evaporation
  Uncommon
    Dry ice
    Naphthalene moth balls

## Slide 39: Acronyms and Terms
VD Vapor Density
VP Vapor Pressure
Sol Solubility
pH Acidity/Alkalinity
Notes: <number>
I. Vapor Density - like specific gravity but for vapors.
< 1 - it floats to the top of the air
> 1 - it sinks below the air
If toluene was present in this room and you squatted down to get something, you would be exposed to much higher levels due to its vapor density relative to air.
II. Vapor Pressure - how much the substance wants to get out of
it’s container. The higher the vapor pressure, the more the substance will be present as a gas.
Alcohol VP vs. motor oil vs. water

## Slide 40: Key Point!
The higher the vapor pressure, the more the risk of off-gassing
The higher the risk of off-gassing, the less persistent the agent is
Less persistent agents pose less contact risk to providers
THUS the higher the contact risk, generally the lower the vapor risk, etc.

## Slide 41: Acronyms and Terms
UEL and LEL
  Upper Explosive/Lower Explosive Limit
FP
  Flash Point
Notes: <number>
Flash point is WITH an ignition source, ignition temp is usually higher for spontaneous ignition…(except eg: white phosphorus). Upper and lower explosive limits are important in that an explosion can’t occur below LEL (too lean), and above UEL (too rich) – if above UEL, ventilation of the area at least for a time will increase the risk of explosion!

## Slide 42: Warning Properties
Odor, eye irritation, or respiratory irritation
Unreliable
  Adequate warning properties may not occur at concentrations < IDLH
  Olfactory fatigue
    Loss of ability to smell a chemical’s odor after a relatively brief period of continued exposure
Notes: <number>
Many very dangerous chemicals have no warning properties. IDLH is Immediate Danger to Life and Health – defined on the next slide!

## Slide 43: Acronyms and Terms
IDLH - Immediate Danger to Life & Health
  Maximum level from which a worker could escape without any escape-impairing symptom or irreversible health effect
PEL - Permissible Exposure Limit
  OSHA standards - therefore are legal limits
  Based on TLV’s and many are identical
  Include 8 hour PEL, 15 minute STEL, and Ceiling
Notes: <number>
I. IDLH — Immediately Dangerous to Life & Health
II. PEL - Permissible Exposure Limit
This one is important because it is an OSHA standard. (TLV – threshold limit value)

## Slide 44: Acronyms and Terms
LD/LC 50
  Lethal Dose 50%
  Lethal Concentration 50%
PPM/MgM3
  Parts Per Million
    measured as volume of contaminant to volume of liquid or air collected in sample
  Milligrams Per Cubic Meter
    measured as weight of contaminant to volume of air collected in sample
Notes: <number>
The lower the numbers the more toxic they are. LD/LC 50 - will kill 50% of those exposed to this dose. PPM/MgM3 - the amount of product in water or air.

## Slide 45: DOT Classification – Transportation Placards
  UN Class # - 1 through 9
    1 = Explosive (TNT)
    2 = Gas (Ammonia)
    3 = Flammable Liquid (Xylene)
    4 = Flammable Solids (Na metal)
    5 = Oxidizer (Oxygen)
    6 = Poison (Chlorine)
    7 = Radioactive ( Gamma, Beta, Alpha)
    8 = Corrosive (Acids, Bases)
    9 = Other Regulated Materials (ORM -D)
Notes: <number>
The Department of Transportation uses the United Nations classification numbering system to more define hazards and the appropriate responses. Class 9 includes riot control agents
The main numbers (1 through 9) are broken down into subcatagories as well.
This classification system is also on placards on vehicles carrying reportable amounts of these chemicals.
Yellow oxidizer, red flammable, white poison

## Slide 46: Fixed Facility Placards
NFPA 704 Marking System
Blue = Health
Red = Fire
Yellow =Reactive
White = Special
Rating 0 through 4
  0 = Nonhazardous
  4 = Very hazardous
Found at fixed chemical locations
Notes: <number>
The most well known hazardous materials placard is the National Fire Protection Association 704 marking system.
The 4 quadrants of the diamond each represent a different hazard type.
Blue is for health
Red for flammability
Yellow for reactivity
White for special warnings such as “Do not contact water”.
Each quadrant is rated on a scale of 0 to 4. 0 represents no hazard and 4 being very hazardous.
For this example, fire/explosion has the greatest concern, followed by reactivity. Health concerns are moderate, but this material cannot be in contact with water or a severe reaction will take place.
The NFPA diamond are found on trucks, buildings containing hazardous materials, storage bins/tanks, or on boxes and shipping containers.

## Slide 47
Notes: <number>
Patients usually do not present to the ED with identifiers for the chemicals involved. Treat the patient’s symptoms!

## Slide 48: Hazard Evaluation
2012 Emergency Response Guidebook
  Quick predictions
  Chemical hazards
Basic first aid information
On-line versions and WISER app for download
vehicles, buildings, containers
Notes: <number>
2012 guidebook, also on-line and Wiser

## Slide 49
Guide 112
Notes: <number>
Emergency Response Guide provides information on hazards, PPE, emergency response, and very basic health care.

## Slide 50: NIOSH Pocket Guide
Concentrates on occupational exposures
Indexed to common agents
Available on-line: http://www.cdc.gov/niosh/npg/default.html
Notes: <number>
May be more helpful than the orange manual for occupational exposures particularly.

## Slide 51: Sources of Info…
Poison Control
1 800 222 1222
Notes: <number>
Poison control should play a BIG role in your information gathering, try to confirm information with more than one source!

## Slide 52: Safety Data Sheets
Changed from MSDS
Standard international format (GHS)
Notes: <number>
A standard MSDS should provide all the physical property data for the chemical, the health hazards, and other information. It must be available at the worksite where the employee is using that chemical.
SDS – 16 categories according to international ‘globally harmonized system’ index – being implemented through until 2016

## Slide 53: Monitoring Devices
pH Paper
G-M counters
Confined Space Meters
  Oxygen
  Combustible Gas
  Carbon Monoxide
  Hydrogen Sulfide
Colorimetric Tubes
Notes: <number>
Training in use of equipment is necessary. Most are irrelevant to the hospital environment except pH paper and GM counters as the concentrations are too low to provide reliable function.
Each device has their limitations.

## Slide 54: Detection
Notes: <number>
Drager tubes can be used to detect chemicals in the air. They are not as accurate in open air environments, and not recommended for use in the hospital environment.

## Slide 55: The biggest problem…
Most exposures present to the ED without a clear toxidrome
The agent is UNKNOWN
In general, the sicker the patient, the more you should consider the patient a risk to YOU prior to decontamination
Notes: <number>
It’s the reverse of what our instincts would tell us – we need to make sure to decon the chemical exposures that are really ill due to their exposure, because if it was that bad for them, it could be bad for you too, especially if the patient is exhibiting a cholinergic toxidrome!

## Slide 56
Notes: 3 dead, 264 injured
<number>

## Slide 57: Explosives
70% of all terrorist incidents involve explosives
They can be used to disperse radiation (and potentially chemicals)
Secondary devices
Notes: <number>
ALWAYS think about radiation and other agents when a bombing occurs.
Picture of backpack or Nick Simpson

## Slide 58: Biological Contamination
Does NOT cause immediate symptoms
Most exposed will not need medical care
Decontamination for powder contamination or suspect aerosol exposure
PAPR with HEPA filter provides good protection if decontamination is required
Notes: <number>
Need for decontamination is rare in biologic events. Only if they have just been exposed to a suspect biologic agent (powder or aerosol) do they need decon. Symptoms occurring within a few hours after exposure indicates anxiety, exacerbation of underlying disease, or a chemical exposure.

## Slide 59: Perimeters & Zones
  Ensure safety and isolation
  Control the scene
  Limit spread of contamination
  Allow for safe working area
Notes: <number>
I. Establishing the Perimeter is essential.
To ensure safety and isolation, limit contamination spread, control scene &
allow for activities such as decontamination.

## Slide 60: HAZMAT Response Zones
Exclusion / Hot Zone
Contamination Reduction / Warm Zone
Support / Cold Zone
YOU are NOT trained to operate in the HOT zone!
You are trained to do decon and contain spills that you recognize / cause ONLY!
Notes: <number>
We are NOT to operate in the HOT zone. The warm zone requires lower levels of PPE (where the hospital is), the Green zone requires no protective equipment.

## Slide 61: HAZMAT Response Zones
Exclusion Zone
Contamination Reduction Zone
Support Zone
Notes: <number>
Zones may vary depending on physical properties of the site, etc. The warm zone may be carried to other locations by fleeing persons. You may move from the cold to the warm zone without moving! (eg: patient comes to you, wind shifts, etc.)

## Slide 62: Always SIN !
For spills and contaminated patients:
  S = Safety
  I = Isolation
  N = Notification
Notes: <number>

## Slide 63: SAFETY (First, last, and always)
Dead people are not heros!
What are the risks?
What do you know?
What don’t you know?
Get the big picture….
Can you handle it?
Notes: <number>

## Slide 64: ISOLATE
Isolate the scene and deny entry.
  If someone has something on them don’t let them go away. If others haven’t been exposed don’t let them have contact with the chemicals
Notes: <number>

## Slide 65: NOTIFY
Internal 911 at HCMC
  Security Supervisor
  Safety Officer On-Call
  Call 911, if necessary – for decon capacity back up and emergency spill response
Notes: <number>
Get help! You need to notify at a minimum these folks, so you can make it somebody else’s problem too!

## Slide 66: Summary
Hospital missions
  Defensive reactions to internal spills
  Victim decontamination for internal or external spills
Recognize an incident
Identify the agent or effects
SIN
  Safety
  Isolate - Limit the damage or spread with physical controls and decontamination
  Notify – HCMC 911 and Charge RN / TCA Staff MD